## Slide 1: Mission Statement
The aim of our project is to design and implement a low-cost human-computer interface (HCI) which allows its user to control the computer cursor with eye movements.

## Slide 2: Project Description
A wearable device that allows the user to control a computer cursor with eye movements
Images of the eye are captured with a digital camera
Images are processed, and mouse movement commands are sent to the computer wirelessly

## Slide 3
Primary:
  Locate the pupil, assign it to one of four quadrants, send movement commands to the computer, move the cursor
  Identify blinking
  Display images that the camera captures
Secondary:
  Support the eye tracker interface with common computer applications
  Display images that the camera captures with overlays that indicate how the images are being processed
  Add more tracking regions for smoother control
  Utilize blinking for operations such as clicking
Tertiary:
  DSP algorithm appropriate for various kinds of lighting
  Utilize glint for more accurate tracking
Goals

## Slide 4: System Block Diagram

## Slide 5: ARM
Several Processors to choose from
VFP (Vector Floating Point)
  Needed for image processing
Popular outside of school
Same processors used in Visions Lab (Sam Siebert)

## Slide 6: ARM vs DSP Chip
Previous teams have used a DSP chip from TI (Rapid Fire)
Use of ARM over that because of bad memory controller on DSP chip
  ARM allows external storage more readily
ARM has all of the facilities that the DSP chip provides in one package

## Slide 7: Beagle Bone
ARM Cortex A8
600 MHz Dual Core
VFP
Minimal peripherals -> Maximum customizability

## Slide 8: Risks
No experience with ARM
  One of the reasons we want to use the ARM
Me killing Arielle
High speed signals if we make our own board for an ARM
  High speed ARMs are difficult to find
a

## Slide 9
Camera
Image Courtesy of Sparkfun
Tentative Camera
CMOS Camera TCM8230MD
640x480 Pixel Resolution
Data Output 8-bit Parallel (YUV or RGB)
Command I/O I2C
Max Frame Rate 30fps
Picture Size: VGA
Note Small Size (Ideal for wearable device)
Retailer: Sparkfun
Price: $9.99
Data Output Rate 144kbps
Purpose
Used to record movements of the eye
Resolution minimal 640x480

## Slide 10
Camera to Microcontroller Interface
Camera control across I2C (uC GPIO)
Synchronization
Glue Logic Solution
CPLD
Data Output 8-bit Parallel
Buffer
Hardware Solution
Shift Registers -> Serial
Latch -> Storage Management
Read from buffer into uC
Additional Microcontroller Solution
Use uC to provide 8-bit Parallel Interface (GPIO Expensive) and other synchronization signals and command

## Slide 11
Camera Block Diagram
(Parallel to Serial)
SDA
SCL
VD
HD
DCLK
8-Bit
Parallel Data
Enable
and Write
Synchronization Signals
I2C Command
8-Bit Serial Data

## Slide 12
Wireless
Purpose
User ‘mobility’
Transmit Cursor Control Commands to Target PC
Tentative Transceiver
Xbee Series 1 Chip Antenna 1mW
Supply Voltage 2.8 – 3.4V
Range 100m
RF Data Rate 250kbps
Serial Data Rate 1200bps- 250kbps
Retailer: Sparkfun
Price: $22.95
XBee Explorer USB (Quick development)
Programming
Retailer: Sparkfun
Price: $24.95
Image Courtesy of Sparkfun

## Slide 13
Wireless Block Diagram

## Slide 14
Risk
RF Exposure (Time and Distance)
1mW Wireless
Power

## Slide 15
Tentative Power
Powered by 120Vac
  Use AC-DC converter
DC-DC converters
  Use DC-DC converters for large step down voltages
Linear Regulators
    Linear Regulators for smaller step down voltages
Isolation of power lines from all components

## Slide 16
Tentative Power
Tentative DC-DC Converters
  Buck Converter
    Covers constant DC input voltages
    Step down 15V to 3.3V
    More efficient than Buck-Boost Converter

## Slide 17
Tentative Power
Tentative DC-DC Converters
  Buck-Boost Converter
    Covers variable DC input voltages
    Suitable for batteries
    Step down 3.3V – 4.3V to 1.2V

## Slide 18
Tentative Power
Camera (2.8V and 1.5V)
ARM CORTEX R4 (1.2V and 3.3V)
ARM CORTEX M4 (1.8V – 3.6V)
IRLED (1.6V)

## Slide 19: Lighting Configuration
Method 1: Infrared lighting configuration
  Use IR emitter attached to glasses to illuminate the eye
  Can achieve “dark pupil” and “light pupil” effect for pupil contrast
  Can experiment with blocking out ambient light or not
Method 2: Ambient lighting configuration
  More difficult but more rewarding
  Challenge: reflections can easily confuse pupil detection algorithms
  Possible Solution: Black felt to control reflections

## Slide 20: Sample Images with Ambient Lighting

## Slide 21
Sample Images with IR Lighting

## Slide 22: Risks
Digital Signal Processing:
  Risks:
    Precision of pupil centroid calculation.
    Inconsistency between pupil and direction of gaze
    Processing time
  Solution:
    Process fewer frames for more thorough processing algorithms.
    Tune via calibration
    Optimize and simplify code as much as possible
Lighting
  Risks:
    Inconsistency in lighting through sequence of images
    Ambient light creating reflections
  Solution:
    Have a controlled lighting environment
    Experiment

## Slide 23: Main Software Flow
Frame?
Yes
Start
Initialization
Control Loop
Frame Interrupt Handler
No

## Slide 24: Interrupt Handler
Blinking?
Get Frame
No
Find pupil center
Comparing center with reference center
Move computer cursor
End Interrupt
Yes

## Slide 25: Initialization
Frame Valid?
No
Capture Frame
Calibration Complete?
Compute Calibration Value
End Calibration
Yes
Send Instruction
Yes
No
List of Calibration Values:
Center position
Region of interest
Skin tone
Eye to eyelid ratio

## Slide 26
Effects of IRLED on eyes
ANSI Z136 – Safe Use of Lasers
Potential Hazards
  Infrared A (780-1400 nm)
    Retinal Burns
    Cataract
  Infrared B (1400 – 3000 nm)
    Corneal Burn
    Aqueous Flare
    IR Cataract
  Infrared C (3000 – 1 million nm)
    Corneal Burn
http://www.microscopyu.com/print/articles/fluorescence/lasersafety-print.html

## Slide 27
Effects of IRLED on eyes
IEC 62471 – Photobiological safety of lamps and lamp systems
For exposure times of t > 1000 s
  Max Exposure limit at 20°C is 200 W/m²
  Max Exposure limit at 25°C is 100 W/m²
Ee = Ie / d²
  Ee is irradiance
  Ie is radiant intensity
  d² is distance
Predicted Ee = 4 W/m²
  SFH 4058 IRLED (Tentative)
Eye Safety of IREDs used in Lamp Applications, Claus Jager, 2010

## Slide 28
Effects of IRLED on eyes
IEC 62471 – Photobiological safety of lamps and lamp systems
4 W/m²
  SFH 4058 IRLED (Tentative)
Exposure times of t > 1000 s
  4 W/m² < 200 W/m² at 20°C
  4 W/m² < 100 W/m² at 25°C
Eye Safety of IREDs used in Lamp Applications; Claus, Jager, 2010

## Slide 29
Effects of IRLED on eyes
Comparison of Lamp versus Laser
http://www.microscopyu.com/print/articles/fluorescence/lasersafety-print.html

## Slide 30: Division of Labor
Tasks | Armeen Taeb | Nick Bertrand | Arielle Blum | Mike Mozingo | Khashi Xiong | Bruce Chen
Software Computer Interface | S | P |  |  |  | 
Lighting/Camera | P | S |  |  |  | 
Pupil Detection Algorithm | P | S |  |  |  | 
Code Optimization | S | P |  |  |  | 
Camera Module |  |  | P | S |  | 
Wireless Communication |  |  | S |  | P | 
Physical Setup |  |  | S |  | P | 
Firmware/Drivers |  |  | P | S |  | 
Power |  |  |  | S | P | 
PCB Layout |  |  |  | P | S | 
Documentation |  |  |  |  |  | 
Mascot/Cheerleader |  |  |  |  |  | P,S,T