## Slide 1: Team eyeCU
Nick Bertrand
Arielle Blum
Mike Mozingo
Armeen Taeb
Khashi Xiong
Notes: Armeen

## Slide 2: Mission Statement
The aim of our project is to design and implement a low-cost human-computer interface (HCI) which allows its user to control the computer cursor with eye movements.
Notes: Armeen

## Slide 3: Project Description
A wearable device that allows the user to control a computer cursor with eye movements
Images of the eye are captured with a digital camera
Images are processed, and mouse movement commands are sent to the computer wirelessly
Notes: Armeen

## Slide 4
Video Eye tracking commonly uses one of two methods:
  Pupil Tracking: (we will focus on this method)
  Glint-Pupil Vector tracking
A: Bright Pupil, B: Dark Pupil, C: Corneal Reflection (glint)
Where Did the User Look?
A
B
C
http://www.sciencedirect.com/science/article/pii/S0262885699000530
Notes: If the illumination is coaxial with the optical path, then the eye acts as a retroreflector as the light reflects of the retina creating a bright pupil effect. If the illumination source is offset from the optical path, then the pupil appears dark because the retroreflection from the retina is directed away from the camera.
Armeen

## Slide 5
Primary:
  Locate the pupil, assign it to one of four quadrants, send movement commands to the computer, move the cursor
  Identify blinking
  Display images that the camera captures
Secondary:
  Support the eye tracker interface with common computer applications
  Display images that the camera captures with overlays that indicate how the images are being processed
  Add more tracking regions for smoother control
  Utilize blinking for operations such as clicking
Tertiary:
  DSP algorithm appropriate for various kinds of lighting
  Utilize glint for more accurate tracking
Goals
Notes: Armeen

## Slide 6: System Block Diagram
Notes: Nick

## Slide 7: DSP Software Flow
Notes: Nick

## Slide 8: Interrupt Handler
Notes: Nick

## Slide 9: Initialization
List of Calibration Values:
  Center Position
  Region of Interest
  Skin Tone
  Eye to Eyelid Ratio
Notes: Nick

## Slide 10: Lighting Configuration
Method 1: Infrared lighting configuration
  Use IR emitter attached to glasses to illuminate the eye
  Can achieve “dark pupil” and “light pupil” effect for pupil contrast
  Can experiment with blocking out ambient light or not
Method 2: Ambient lighting configuration
  More difficult but more rewarding
  Challenge: reflections can easily confuse pupil detection algorithms
  Possible Solution: Black felt to control reflections
Notes: Nick

## Slide 11: Sample Images with Ambient Lighting
Notes: Nick

## Slide 12
Sample Images with Infrared Lighting (Dark Pupil)
Notes: Nick

## Slide 13: Risks
Digital Signal Processing
  Risks
    Precision of pupil centroid calculation
    Inconsistency between pupil and direction of gaze
    Processing time
  Solution
    Process fewer frames for more thorough processing algorithms
    Tune via calibration
    Optimize and simplify code as much as possible
Lighting
  Risks
    Inconsistency in lighting through sequence of images
    Ambient light creating reflections
  Solution
    Have a controlled lighting environment
    Experiment
Notes: Nick

## Slide 14: Effects of IRLED on Eyes
ANSI Z136 – Safe Use of Lasers
Potential Hazards
  Infrared A (780nm – 1400 nm)
    Retinal Burns
    Cataract
  Infrared B (1400nm – 3000 nm)
    Corneal Burn
    Aqueous Flare
    IR Cataract
  Infrared C (3000nm – 1 million nm)
    Corneal Burn
http://www.microscopyu.com/print/articles/fluorescence/lasersafety-print.html
Notes: Khashi

## Slide 15: Effects of IRLED on Eyes
IEC 62471 – Photobiological safety of lamps and lamp systems
For exposure times of t > 1000s
  Max exposure limit is 200 W/m² at 20°C
  Max exposure limit is 100 W/m² at 25°C
Ee = Ie/d²
  Ee is irradiance
  Ie is radiant intensity
  d is distance from IRLED to eye
Predicted Ee = 312mW/m²
  SFH 484 IRLED (Tentative)
Eye Safety of IREDs used in Lamp Applications, Claus Jager, 2010
Notes: Khashi

## Slide 16: Effects of IRLED on Eyes
IEC 62471 – Photobiological safety of lamps and lamp systems
312mW/m²
  SFH 484 IRLED (Tentative)
For exposure times of t > 1000s
  312mW/m² < 200 W/m² at 20°C
  312mW/m² < 100 W/m² at 25°C
Eye Safety of IREDs used in Lamp Applications, Claus Jager, 2010
Notes: Khashi

## Slide 17: Effects of IRLED on Eyes
Lamp vs Laser
http://www.microscopyu.com/print/articles/fluorescence/lasersafety-print.html
Notes: Khashi

## Slide 18: System Block Diagram
Notes: Khashi

## Slide 19: Power
Powered by 120 Vac
  Use AC-DC converter
DC-DC converters
  Use DC-DC converters for larger voltage step downs
Linear Regulators
  Linear Regulators for smaller voltage step downs
Isolation of power lines from all components
Notes: Khashi

## Slide 20: Power
Tentative DC-DC Converters
Buck Converter
  Efficient with constant DC input voltages
  Ideal for 15V to 3.3V step down
  More efficient than Buck-Boost Converter
Notes: Khashi

## Slide 21: Power
Tentative DC-DC Converters
Buck-Boost Converter
  Ideal for variable DC input voltages (batteries)
  Step down 3.3V – 4.3V to 1.2V
Notes: Khashi

## Slide 22: Power
Camera
  2.8V and 1.5V
ARM CORTEX R4
  1.2V and 3.3V
ARM CORTEX M4
  1.8V to 3.6V
IRLED
  1.6V
XBEE
  2.8V to 3.4V
Notes: Khashi

## Slide 23: Risk
Power
  Risk
    Surge from AC-DC converter, potentially destroying components or shocking user
  Solution
    Fuse the AC-DC converter so a power surge does cause damage
Notes: Khashi

## Slide 24: System Block Diagram
Notes: Mike
-- describe glasses + camera
-- talk about camera board + XBEE
-- follow data through ARM, talk about DSP here.
-- Mention data storage for debugging help
-- Interface to computer
-- program on host computer to intercept control signals and control the cursor

## Slide 25: ARM
VFP (Vector Floating Point)
Popular outside of school
  Gain good experience
Same processors used in Visions Lab
  Sam Siewert as a great resource
Wide Range of processors
  Cortex M4, Cortex R4, Cortex A8*
    *Cortex A8 is the processor used on the BEAGLE boards
Notes: Mike
-- Our DSP will need some sort of floating point or fixed point (integer calculations not sufficient)

## Slide 26: ARM vs DSP Chip
Previous teams have used a DSP chip from TI
  Rapid Fire used a DSP chip
Use of ARM over that because of difficult memory controller on DSP chip
  ARM will allow external storage more readily
ARM has all of the facilities that the DSP chip provides in one package
  Fewer components to worry about
Notes: Mike
-- DSP chip that rapid fire used had a clock of 300MHz
-- only for high speed memory (data storage)
-- fewer components in that we will have only the ARM, instead of a microcontoller + DSP chip.
-- does not include supporting components

## Slide 27: Beagle Board
3 boards to chose from
  BEAGLE, XM, Bone
Using the BEAGLE bone
  Fewer included components
  USB and Ethernet
Use as main board
  Build interface to the board
As fallback plan
  Layout our own ARM board, and if we can’t get it to work, utilize the BEAGLE
Notes: Mike
-- uses cortex A8 processor
-- speed of 600MHz

## Slide 28: Risks
No experience with ARM
  An opportunity to gain experience
High speed signals if our team designs our own board for the ARM
  Signal Integrity
  Finding a high speed arm that is not a BGA
Notes: Mike
-- cortex M4 ~180 MHz
-- cortex R4 ~200 MHz

## Slide 29: System Block Diagram
Notes: Arielle

## Slide 30: Wireless
Transmit camera data to host controller
Xbee Series 1 Chip
  Range 100m
  RF Data Rate 250 kbps
  Serial Data Rate 1200 bps – 250 kbps
  Xbee Explorer USB
    Quick Development
Notes: Arielle
-- from SparkFun
-- two points of interest
-- range = plenty enough
-- speed -> based on calculation of maximun data output from camera
we do not exceed 250 kbps so the XBEE will be able to
transmit all of the images with no slowing

## Slide 31: Wireless Block Diagram
Notes: Mike

## Slide 32: Risk
Insufficient transmit speed
RF Exposure (Time and Distance)
  1mW Wireless
Notes: Mike
-- like mentioned before based on the quick calculation we did we should have sufficient bandwidth to
transmit all of the images
-- low power, consider cell phones which have power ratings around 1 Watt

## Slide 33: System Block Diagram
Notes: Arielle

## Slide 34: Camera
Used to record movements of the eye
Tentative Camera
  TCM8230MD CMOS Camera
  Small, ideal for a wearable device
  640 x 480 Pixel Resolution (VGA)
  30 FPS (Frames Per Second)
  Command I/O 12C
  Data Output 8-bit Parallel (YUV or RGB)
  Data Output Rate 144kbps
Notes: Arielle

## Slide 35: Camera
Controlled across I2C (uC GPIO)
Synchronization
Data Output 8-bit
  Buffer
  Hardware Solution
    Shift Registers -> Serial
    Latch -> Storage Management
    Read from buffer into uC
  Additional Microcontroller Solution
    Use uC to provide 8-bit Parallel Interface with other synchronization signals and command
Notes: Arielle

## Slide 36: Camera Block Diagram
Notes: Arielle

## Slide 37: Project Expenses
Section | Component | Quantity | Cost ($)
Wireless |  |  | 
 | XBee | 2 | 22.95
 | USB XBee Explorer | 1 | 24.95
 | XBee Breakout Board | 2 | 2.95
Processing |  |  | 
 | BeagleBone Evaluation Board | 1 | 89
 | I/O Board | 1 | 33
 | XBee Microcontroller (ARM) | 1 | 1
 | SDRAM | 1 | 10
Mechanical |  |  | 
 | Lensless Glasses | 1 | 5.99
Camera |  |  | 
 | 640x480 CMOS Camera | 1 | 9.99
 | Test Cameras | 3 | Donated
 | FTDI to USB | 1 | 10
 | Glue Logic CPLD | 1 | 2
 | Hardware Buffer | 2 | 1.5
 | IR LEDS | 4 | 0.95
Manufacturing |  |  | 
 | PCB Fabrications (3 at 4 layer, 2 at 2 layer) | 5 | 264
Presentation | Poster | 1 | 55
Misc. |  |  | 200
Total Cost |  |  | 735.16
Notes: Arielle

## Slide 38: Sustainability and Environmental Concerns
RoHS

## Slide 39: Division of Labor
Tasks | Armeen Taeb | Nick Bertrand | Arielle Blum | Mike Mozingo | Khashi Xiong | Bruce Chen
Computer Applications | S | P |  |  |  | 
Lighting | P | S |  |  |  | 
DSP | P | S |  |  |  | 
Code Optimization | S | P |  |  |  | 
Camera Module |  |  | P | S |  | 
Wireless Communication |  |  | S |  | P | 
Physical Setup |  |  | S |  | P | 
Firmware/Drivers |  |  | P | S |  | 
Power |  |  |  | S | P | 
PCB Layout |  |  |  | P | S | 
Mascot/Cheerleader |  |  |  |  |  | P,S,T
Primary | Secondary
Notes: Arielle

## Slide 40: Questions?
Notes: Arielle